## Slide 1: Energy Efficiency Goals Recommendation
City Council
January 28, 2013
Item 11

## Slide 2: Legislative and Policy
Legislative Energy Efficiency Requirements
  Assembly Bill 2021 (2006)
    Goals for 2014-2023 due to CEC March 15, 2013
  Assembly Bill 2227 (2012)
  Senate Bill 1037 (2005)
  Assembly Bill 32 (2006)
City Policy
  Power Supply 2012 Integrated Resource Plan
  Urban Environmental Accords Goals
California’s “Loading Order” Policy

## Slide 3: Energy Efficiency Resource Assessment Model (EERAM)
Spreadsheet Model
  Developed by Navigant Consulting
  Customized for each CMUA member
  Used for California IOU’s (CPUC) study
Estimates Potential For Energy Efficiency
  “Market potential” is used as benchmark for goals
Consultant Applied “Aggressive” Parameters to Configure PWP’s EERAM Model

## Slide 4: Recommended EE Goals
Annual Energy Efficiency Program Goals (incremental):
  More than 1% of annual retail energy sales; and
  0.7% peak demand reduction
 | 2007 Goal | 2010 Goal | 2013 Market Potential | Proposed Goal | Change from 2010
Energy Savings (MWh/year) | 18,126 | 16,600 | 12,654 | 12,750 | -23%
Demand Reduction (MW/year) | 2.2 | 3.8 | 2.2 | 2.3 | -40%

## Slide 5: PWP’s Energy Efficiency Goals (MWh/year)
Chart: 
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
2007 Goals | 10000 | 13500 | 17000 | 22626.5883 | 22626.5883 | 22626.5883 | 22626.5883 | 22626.5883 | 22626.5883
2010 Goals | 14500 | 14500 | 14500 | 17500 | 17500 | 17500 | 17500 | 17500 | 17500 | 17500
Market Potential | 12731.1371 | 12528.0754 | 12470.6482 | 13120.9348 | 13046.4893 | 13271.1022 | 13307.2094 | 12977.4717 | 12146.2945 | 10938.2395
Proposed 2013 Goal | 12750 | 12750 | 12750 | 12750 | 12750 | 12750 | 12750 | 12750 | 12750 | 12750

## Slide 6: Demand Reduction Goals
Market Potential Declined More than Energy
  Each program “measure” has its own calculated demand reduction value
  Mix of cost-effective measures selected have lower peak demand impacts
  Peak heavy measures: Tougher codes and standards targeted – less potential remains
  Behavioral programs: No peak reduction value
  Less commercial space in model

## Slide 7: Cost to Achieve Goals
EERAM Model Predicts ~ $4.5 M/year on Avg.
PWP Anticipates:
  $3.5 – 4.5 M per year over ten-year period
  Approximately $3.5 M for FY2014
  Greater than 2% of retail revenues
Funding from PBC Fund (410):
  Cost-effective energy efficiency and demand reduction
  Pasadena Solar Initiative (“PSI”)
  Research, development and demonstration projects
  Low income rate assistance and energy efficiency programs

## Slide 8: Comparative Goals
Targets for IOU’s
  2014-2023 cycle under consideration by CPUC
  Market potential approximately 0.9% of energy sales
  IOU’s also credited with “Codes and Standards” impact – raises potential to ~1.5% of energy sales
PWP On the “Higher Side” of POU Goals
    SMUD and Palo Alto are higher/similar
    Average results/proposed goals for POU’s using EERAM
      Median 0.50% of sales
      Average 0.53% of sales
      Load-Weighted Average 1.0% of sales

## Slide 9: Environmental Community View
NRDC “Aggressive” Goals
  Annual electric savings > 1% of sales
  Efficiency investments > 2% of revenues
Proposed Goals
  Annual electric savings exceed 1% of forecast sales
  Estimated efficiency program cost equivalent to approximately 2 to 2.5% of retail electric revenues

## Slide 10: Potential PBC Rate Impact
PBC Rate Impact:
  Potential funding gap up to $1.1 million in FY2014; or
  Up to 0.1¢/kWh ($0.50/month for 500 kWh/month customer)
Will Depend Upon Future Council Actions
  Adopted budget for PBC Fund
  Variables Include Whether to Fully Fund:
    Energy efficiency programs to meet goals
    Continued solar program incentives to meet goals
    RD&D programs
    Rate assistance program to meet demand
Other Potential Mitigating Factors:
  Carryover PBC Fund balance available from FY2013
  Retail sales volume increase (economic recovery)

## Slide 11: Recommended Action
Adopt the Proposed Ten-Year Energy Efficiency Program Goals for FY2014-FY2023:
  12,750 MWh per year energy savings
  2.3 MW per year peak demand reduction

## Slide 12: Backup Slides
PBC and Costs
Actual EE
Load Impacts

## Slide 13: Annual PBC Expenditures ($000)
Chart: 
| FY2008 Actual | FY2009 Actual | FY2010 Actual | FY2011 Actual | FY2012 Actual | FY2013 Projected* | FY2014 Prelim
Rate Assistance | 314.497 | 462 | 610 | 686 | 773 | 775 | 775
RD&D | 208.3764 | 320 | 102 | 107 | 92 | 200 | 176
Other | 565.6418 | 511 | 466 | 341 | 377 | 402 | 425
Solar | 474.1188 | 834 | 1385 | 1935 | 2629 | 3290 | 3000
Efficiency | 1301.1301 | 6032 | 4569 | 3266 | 3222 | 3900 | 3450
Total PBC Revenues | 3563.377 | 7371.3782 | 6927.9621 | 6729.0815 | 6525.2101 | 6778.827 | 6700
Gap

## Slide 14: EE Program “First Year” Cost
Chart: Avg Cost ($/kWh)
| FY 2010 | FY 2011 | FY 2012 | FY 2013 | FY 2014
Overhead | 0.023708 | 0.028147 | 0.030224 | 0.031034 | 0.039216
Incentives | 0.28805 | 0.23859 | 0.21976 | 0.23793 | 0.23137
Energy Savings | 14655.54 | 12244.298 | 13069 | 14500 | 12750
Average energy efficiency program costs are fairly stable

## Slide 15: PBC Rate
PBC Rate Adopted in 1996
  Initially fixed at 0.271¢/kWh
Rate Modified in 2007
  Formula based
  Adjusts for approved budget, fund balance, sales
  0.573¢/kWh (since FY2009)
  Generates ~$6.7 million annual revenue

## Slide 16: Cumulative Energy Efficiency (MWh and % of Retail Sales)
Chart: Fiscal Year
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Cumulative Projected | 0 | 0 | 0 | 0 | 0 | 89203.5965 | 101953.5965 | 114703.5965 | 127453.5965 | 140203.5965
Cumulative Actual | 8175.9625 | 34734.7585 | 49390.2985 | 61634.5965 | 74703.5965
Cumulative Goal | 0.0083333 | 0.019583 | 0.03375 | 0.045833 | 0.057917 | 0.07 | 0.080625 | 0.09125 | 0.10187 | 0.1125
Cumulative Goals Exceeded

## Slide 17: Retail Sales and Cumulative Efficiency Fiscal Year Basis (GWh/Year)
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Net Retail Sales | 1233.9158 | 1238.6258 | 1241.4958 | 1178.0048 | 1148.8634 | 1114.9781 | 1126.5302 | 1119.0302 | 1137.4882 | 1134.4079 | 1128.2347 | 1122.0933 | 1115.9836 | 1109.9058 | 1103.8602 | 1097.8469 | 1091.866
Actual Efficiency | 4.281 | 12.457 | 39.0158 | 53.6713 | 65.9156 | 78.9698
Forecast Efficiency | 93.4698 | 105.9698 | 118.4698 | 130.9698 | 143.4698 | 155.9698 | 168.4698 | 180.9698 | 193.4698 | 205.9698 | 218.4698
2012 IRP Net Sales | 1129.6532 | 1133.3597 | 1128.5178 | 1120.793 | 1110.1115 | 1099.4603 | 1088.8394 | 1078.2491 | 1079.6395 | 1081.0607 | 1082.513
Actual net retail sales are declining

## Slide 18: More Backup Slides
Details
  Backup
  Reference

## Slide 19: Key Policy Considerations
Straightforward?
  Fixed MWh target simple to understand – no debate
How Aggressive?
  Utility goal comparisons
  Environmental advocacy group “target”
How Feasible?
  Navigant EERAM model “Market Potential”
  PWP program experience
Tolerable Rate Impacts?
  Up to 0.1¢/kWh (50¢/month for 500 kWh customer)

## Slide 20: Policy Background
PWP’s Energy Efficiency Programs are Consistent With and Support:
  Power Supply 2012 Integrated Resource Plan
  Urban Environmental Accords Goals
    Peak load reduction, GHG reduction
  Green City Action Plan
  Mayor’s Climate Initiative
  National Action Plan for Energy Efficiency
  California’s “Loading Order” Policy
    Acquire all cost effective energy-efficiency prior to any supply-side (generation) resources

## Slide 21: Legislative Background
Assembly Bill 2021 (2006)
  10-year efficiency and demand reduction goals
  Report goals, spending, and progress to the California Energy Commission (CEC)
  Council must adopt energy efficiency goals every three years:
    Next up: Goals for 2014-2023 due to CEC March 15, 2013
Assembly Bill 2227 (2012)
  New energy efficiency goals every four years starting 2017
  Consolidates certain reporting requirements
Senate Bill 1037 (2005)
  Utilities must acquire all cost effective energy efficiency prior to any other resources
Assembly Bill 32 (2006)
  Reduce GHG emissions to 1990 levels by 2020
  Energy efficiency a major compliance tool

## Slide 22: Collaborative Goal Development
Joint Effort by 36 California Utilities
  California Municipal Utilities Association (CMUA)
  Northern California Power Agency (NCPA)
  Southern California Public Power Authority (SCPPA)
Retained Consultant to Develop Model
  Determine energy efficiency and demand reduction targets for each individual utility
  Rocky Mountain Institute retained for 2007 effort
  Navigant (Summit Blue) retained for 2010 and 2013

## Slide 23: Market Potential (MWh)
Current Forecast w/Actual 2006-2011 Results
  2010 Goal (2011-2013) 14,500 MWh; (2014-2020) 17,500 MWh
  2013 Goal (2014-2023) 12,750 MWh
Chart: 
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Actual | 4251.0502 | 4281 | 8175.9625 | 26558.796 | 14655.54 | 12244.298 | 13069 | 13731.2133
Forecast-Incremental | 13731.2133 | 12731.1371 | 12528.0754 | 12470.6482 | 13120.9348 | 13046.4893 | 13271.1022 | 13307.2094 | 12977.4717 | 12146.2945 | 10938.2395 | 9751.906

## Slide 24: Market Potential
~30% Lower than 2010 Study
Primary Drivers:
  Changes in Codes and Standards have decreased technical potential by about 10%
  Reduced savings for many energy retrofit “measures” (lighting, refrigerator recycling) in DEER database
  Improved method for estimating commercial sector floor space:
    Corrected overstatement of PWP’s commercial floor space estimates in 2010 EERAM

## Slide 25: Market Potential
Other Model Changes Tending to Increase the Forecast Market Potential:
  Inclusion of behavioral program effects (like OPower)
  Inclusion of more new and emerging technologies
Behavioral Programs Significant Contributors

## Slide 26: Energy Efficiency Resource Assessment Model (EERAM)
Navigant Consulting

## Slide 27: Energy Efficiency Resource Assessment Model (EERAM)
Spreadsheet model customized for each utility
Estimates technical, economic, and market potential
  “Market potential” is used as benchmark for goals
Provides results for
  Residential,
  Commercial, and
  Industrial sectors

## Slide 28: EERAM: Utility-Specific Inputs
Financial Parameters and Rates
Building Stock, Past Efficiency Program Efforts
Efficiency Measure Impacts/Costs from the Most Recent DEER Database (CEC/CPUC)
New and Emerging Technology
SCE’s Avoided Costs Adopted by CPUC
  Generally higher than PWP’s avoided costs
  Results in slightly higher energy efficiency “market potential” (a few more measures pass TRC test)

## Slide 29: Key Modeling Variables
Modify the Market Potential Based on Utility History Desire to be Aggressive
  PWP’s variables amongst the most aggressive of POUs
These include:
  Calibration method (aligns model output for utility)
  TRC screen value (what is “economic”)
  Re-participation estimates (“repeat” incentives)
  Maximum market penetration (willingness * awareness)
  Diffusion curve coefficients (adoption rates for new technology)

## Slide 30: EERAM - Approach
Two methods for estimating market potential
  For existing measures, a consumer choice algorithm based on measure payback with the elasticity coefficient calibrated to past achievements by PWP
  New and emerging technologies do not have past program accomplishments for coefficient calibration
    Bass diffusion curve utilized with the curve based on coefficients identified by Dr. Bass as representing the diffusion of new technologies into the market place

## Slide 31: EERAM - Utility-Specific Inputs
Financial parameters and rates
Building stock, past efficiency program efforts
Efficiency measure impacts and costs are primarily from the most recent DEER database
New and emerging technology impacts and costs generally from various utility work-papers
SCE avoided costs adopted by CPUC were used for the TRC screen
  These are generally higher than PWP’s avoided costs
  Results in slightly higher energy efficiency “market potential” (a few more measures pass TRC)

## Slide 32: Utility Level Modeling Variables
Some key input variables are used to modify the market potential based on utility history and a utility’s desire to be aggressive.
These include:
  Calibration method
  TRC screen value; both for existing technologies and new/emerging technologies
  Re-participation estimates
  Maximum market penetration (willingness * awareness)
  Diffusion curve coefficients

## Slide 33: EERAM Calibration Method
Choices are among:
  The last year(s) of available data (2010, 2011, average)
  Percent of sector sales
PWP is utilizing percent of sales
  Calibration is used to set the payback coefficient by measure. Moving forward, the percent of sales in the market potential is dependent on the decision algorithms and how codes and standards and other outside influences affect adoption
  The calibration percent values used for PWP are in the top five percent of what other POUs utilized

## Slide 34: EERAM
TRC Screen
  For existing technologies, PWP used 0.75
  For emerging technologies, PWP used 0.5
    About 90 percent of the other POUs used these values
    These values were used by the IOUs
Reparticipation
  PWP assumes no re-participation (0%) by our customers
    PWP closely monitors prior participation when processing rebate requests
    Values used by other POUs varied widely, from 0.0% to 60%
Maximum market penetration (willingness * awareness)
  85% is most often used as the maximum a market can be penetrated.
    Nearly all POUs utilized 85%.
    PWP uses 90% as it believes its population is more environmentally conscious

## Slide 35: Diffusion Curve Variables
The curve function has four primary variables:
  The starting level for the program
  The coefficient of innovation: external influences and/or advertising effect
  The coefficient of imitation: internal influence or word-of-mouth effect
  The maximum savings that can be achieved
PWP values
  Starting level 3.5% of maximum savings. Most other POUs used 3%. Rational being the population is more environmentally conscious
  According to the literature, the coefficient of innovation can vary from 0.1 to 0.3. PWP used 0.15, which is on the faster adoption side of the range
  According to the literature, the coefficient of innovation can vary from 0.2 to 0.5. PWP used 0.4 which is on the faster adoption side of the range
  Maximum savings is set as technical potential multiplied by willingness * awareness
Values used by other POUs varied significantly.
  Small, rural utilities: “slower” adoption side of the acceptable range
  Larger, urban utilities: “faster” adoption side of the acceptable range

## Slide 36: Market Potential
Changing Shares Over Time for Existing and New /Emerging Technologies and the Behavioral Program
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Current-Tech | 11644.636 | 11346.3281 | 10609.2862 | 8871.463 | 7968.439 | 7158.658 | 6650.5119 | 5875.2002 | 5711.6472 | 5616.6762 | 5464.9636 | 5114.9023 | 4588.5882 | 4131.7777
New and Emerging-Tech | 554.3893 | 810.683 | 1123.1828 | 1874.1655 | 2574.1279 | 3326.4816 | 4079.289 | 4195.1553 | 4563.8352 | 4675.4275 | 4477.9166 | 3977.3147 | 3276.0881 | 2527.079
Behavior | 45.273 | 1694.3231 | 1694.3231 | 1694.3231 | 1694.3231 | 1694.3231 | 2099.9484 | 2749.6562 | 2769.1421 | 2788.628 | 2808.1139 | 2827.5998 | 2847.0857 | 2866.5716

## Slide 37: Market Potential
Changing Mix of Source for Market Potential
  Most of the new and emerging technologies are for the residential sector
  Behavioral program is currently modeled as residential
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Residential | 1587.8417 | 4365.9601 | 4374.5544 | 4133.8471 | 4468.9318 | 4840.9207 | 5716.7458 | 6274.3476 | 6686.2848 | 6995.0717 | 7084.7849 | 6883.8272 | 6402.9875 | 5772.2488
Commercial | 11277.918 | 9803.031 | 9356.6589 | 8597.29 | 8059.1436 | 7629.7274 | 7404.189 | 6772.1417 | 6584.8174 | 6312.1377 | 5892.6868 | 5262.4672 | 4535.252 | 3979.6571

## Slide 38: Market Potential
Top 20 Measures - 2014
Rank | Top Twenty Measures - 2014 | 2014 - Energy Savings (MWh) | Energy % of Total
1 | Com - Advanced Generation T8 - 4ft | 2,846 | 22.4%
2 | SFE - Home Energy Report | 1,694 | 13.3%
3 | Com - Combination Oven | 523 | 4.1%
4 | Com - High Performance Rooftop Unit | 375 | 2.9%
5 | Com - Linear fluorescent delamping 4 ft | 369 | 2.9%
6 | LI - Low Income | 291 | 2.3%
7 | Com - T12 to T8 - 4ft | 254 | 2.0%
8 | SFE - Recycle refrigerator | 248 | 1.9%
9 | Com - PS Exterior HID - Mercury Vapor Base | 233 | 1.8%
10 | SFE - HVAC Quality Maintenance | 229 | 1.8%
11 | Com - LED Exit sign | 226 | 1.8%
12 | Com - CFL Fixture Under 15W | 224 | 1.8%
13 | Com - High bay fluorescent | 216 | 1.7%
14 | Com - Comprehensive Commercial HVAC Rooftop Unit Quality Maintenance | 208 | 1.6%
15 | Com - LED Lighting T8 - 4ft Equiv | 173 | 1.4%
16 | Com - Pressureless Steamer | 150 | 1.2%
17 | Com - EMS | 146 | 1.1%
18 | Com - CFL Fixture 16 to 24W | 133 | 1.0%
19 | Com - Retro commissioning | 127 | 1.0%
20 | Com - Linear fluorescent delamping 8 ft | 124 | 1.0%
 | Top 20 Total | 8,788 | 69.0%

## Slide 39: Market Potential
Top 20 Measures - 2023
Rank | Top Twenty Measures - 2023 | 2023 - Energy Savings (MWh) | Energy % of Total
1 | SFE - Home Energy Report | 2,847 | 26.0%
2 | SFE - HVAC Quality Maintenance | 891 | 8.1%
3 | Com - Combination Oven | 639 | 5.8%
4 | Com - High Performance Rooftop Unit | 548 | 5.0%
5 | SFE - Smart Strip | 416 | 3.8%
6 | Com - Kitchen Vent Hoods | 404 | 3.7%
7 | SFE - Effcient Set Top Box | 396 | 3.6%
8 | Com - Retro commissioning | 370 | 3.4%
9 | Com - Improved Data Center Design | 344 | 3.1%
10 | MFE - Smart Strip | 338 | 3.1%
11 | MFE - HVAC Quality Maintenance | 256 | 2.3%
12 | Com - Variable-Speed CRAC Compressors | 229 | 2.1%
13 | LI - Low Income | 226 | 2.1%
14 | Com - LED Lighting T8 - 4ft Equiv | 207 | 1.9%
15 | Com - Pressureless Steamer | 183 | 1.7%
16 | MFE - Effcient Set Top Box | 179 | 1.6%
17 | Com - Dimmable w/F32T8 & 5W standby CFL lamps | 143 | 1.3%
18 | Com - Key Card Control Option B (HVAC Only) | 134 | 1.2%
19 | Com - Food Holding Cabinet | 133 | 1.2%
20 | Com - Cool Roof | 131 | 1.2%
 | Top 20 Total | 9,013 | 82.4%

## Slide 40: 2010 Adopted Goals
Highest of All Utilities in CMUA
Fiscal Years 2011 Through 2013
  14,500 MWh per year (approx 1.1% of load)
  3.3 MW per year peak energy demand reduction
  Maintained current PBC rate
Fiscal Years 2014 Through 2020
  17,500 MWh per year (approx 1.3% of load)
  4.2 MW per year peak energy demand reduction
  PBC rate increase would be needed to achieve this goal

## Slide 41: 2010 Goal Comparison with Other CMUA Utilities
Average

## Slide 42: Rate Pressures
Rate Component | ~Rate | Rate Pressures
PBC | 0.58¢ | Solar, Low-Income, and Energy Efficiency Programs
Energy | 8.53¢ | Renewable Resources Fuel Costs GHG Mitigation, Credits/Tax
Transmission | 0.82¢ | CA Transmission Grid Expansions to Support Reliability and Deliver Renewable Resources
Distribution | 4.28¢ | Aging Infrastructure Replacement Distr. Grid Modernization Reliability Enhancement

## Slide 43: Environmental Community View
NRDC White Paper - March 9, 2010
“California Restores Its Energy Efficiency Leadership”
  Policies that properly align incentives drive utilities to implement aggressive efficiency programs
  The legislature and CPUC have adopted the policies necessary to spur aggressive efficiency programs for the IOUs. The result is that they now have truly aggressive programs based on industry-standard efficiency metrics with:
    annual electric savings > 1% of sales
    efficiency investments > 2% of revenues